## Slide 1
GITAM UNIVERSITY
AY 2021-25
Major Project
A University should be a place of light, of liberty, and of learning.
www.gitamedu.com
Department of Electrical Electronics and Communication Engineering
Two Dimensional Histogram Based Bi-level Image Segmentation
Project Team:
SUCHITHRA C
S.CHARISMA SULTHANA
P.SIREESHA
Project Mentor:
DR. PANKAJ KANDHWAY

## Slide 2
Project Group – Details
Photo
Track
Roll No
Name
EECE AI/ML
BU21EECE0100426
SUCHITHRA.C
EECE AI/ML
BU21EECE0100356
CHARISMA SULTHANA.S
EECE AI/ML
BU21EECE0100210
SIREESHA.P

## Slide 3
Objective and Goals
Objective
Goals
The objective of this study is to enhance image segmentation accuracy by incorporating contextual information into traditional thresholding methods. Specifically, the goal is to develop a new segmentation approach that combines pixel brightness with local relative entropy-based contextual information from neighboring pixels. This method aims to improve the differentiation of regions with similar brightness levels.
Main Goals
Develop a Novel Image Segmentation Method
Integrate pixel brightness with local relative entropy-based contextual information to enhance segmentation accuracy.
Optimize Thresholding Using Cross-Entropy Minimization
Implement a two-dimensional histogram to determine optimal threshold values for effective segmentation.
Additional Goals
Quantitative Analysis: Assess performance using SSIM, FSIM, PSNR, and entropy.
Benchmarking: Compare the new method with existing segmentation techniques to evaluate its relative strengths and weaknesses.

## Slide 4
Literature Survey
Literature Review on Two-Dimensional Histogram-Based Bi-Level Image Segmentation
Abstract Traditional thresholding methods, in image segmentation often produce poor results as they rely solely on pixel brightness. To improve segmentation accuracy, a new method will be explored where both pixel brightness and local relative entropy bused contextual information of neighboring pixels will be designed. This approach will construct a two-dimensional histogram based on pixel brightness and contextual information, which quantifies brightness differences between a pixel and its neighbours. This additional contextual information will help differentiate regions with similar brightness. By plotting each pixel based on these values, the method reflects individual pixel intensities and local brightness variations based on neighboring information. The optimal threshold value for bi-level segmented image will be determined by minimizing cross-entropy. For subjective analysis, the segmented image will be compared with its ground true and several image segmentation techniques. The SSIM, FSIM, PSNR, and entropy parameters will be explored for quantitative analysis.

## Slide 5
s.no | TITLE | AUTHOR | YEAR OF PUBLISHING | DRAWBACKS
1. | Two-Dimensional Histogram-Based Bi-Level Image Segmentation | Xu Ding and Jie Chen. | October 2002 | High Computational Cost Sensitivity to Image Noise Limited to Bi-Level Segmentation Memory Intensive
2. | Digital Image Processing | Rafael C. Gonzalez and Richard E. Woods | August 28, 2007 (3rd Edition) | The book covers a broad range of topics, which might be overwhelming for beginners. Some advanced topics may lack detailed explanations and might require supplementary reading.
3. | Image Segmentation and Feature Extraction | Mark Nixon | April 22, 2013 | Focuses primarily on feature extraction alongside segmentation, which might not be ideal if you are looking for in-depth coverage of segmentation techniques only. The book assumes a fair amount of prior knowledge in image processing and may not be suitable for complete beginners.

## Slide 6
 | TITLE | AUTHOR | YEAR OF PUBLISHING | DRAWBACKS
4. | Image Segmentation: A Survey of Graph-Cut Methods | Yuri Boykov and Vladimir Kolmogorov | September 2003 | It does not provide in-depth explanations of each method, rather it focuses on comparing various graph-cut approaches. It doesn’t cover recent advancements since its publication.
5. | Image Processing, Analysis, and Machine Vision | Milan Sonka, Vaclav Hlavac, Roger Boyle | February 2014 (4th Edition) | Broad Scope: The book covers a wide range of topics, which may result in a more general overview rather than an in-depth exploration of bilevel image segmentation. Dated Content: The book was published in 2014, and newer methods or tools may not be included. Complexity: Like many textbooks in this field, it requires a strong background in mathematics and image processing.
6. | Image Segmentation: Advanced Concepts and Practical Applications | Vipin Tyagi | September 2018 | Advanced Level: The content is more suitable for advanced learners or professionals, which can be a barrier for beginners. Limited to Specific Techniques: The book focuses on advanced segmentation techniques, which might not include the most basic bilevel methods in sufficient detail. Complexity level is high to understand

## Slide 7
Literature Survey
REFERENCE :-
1.Otsu, N. (1979). A threshold selection method from gray-level histograms. IEEE Transactions on
Systems, Man, and Cybernetics.
2. Pal, N. R., & Pal, S. K. (1989). Entropic thresholding. Signal Processing.
3. Liao, P. S., Chen, T. S., & Chung, P. C. (2001). A fast algorithm for multilevel thresholding. Journal
of Information Science and Engineering.
4. Cheng, H. D., & Chen, Y. H. (2004). Fuzzy partitioning of two-dimensional histograms for
thresholding. Pattern Recognition.
5. Zhu, W., Huang, Y., & Chen, Y. (2017). Hybrid methods for segmentation of medical images using
deep learning and two-dimensional histograms. IEEE Access.

## Slide 8
Analysis - SWOT
1. Enhanced Accuracy
2. Two-Dimensional Histogram
3. Optimal Thresholding
Strengths
Weaknesses
1. Increased Complexity
2. Computational Cost
3.Parameter Sensitivity
Threats
1.Complexity vs. Usability
2.Overfitting to Training Data 3.Competition from Advanced Methods
Opportunities
1.Improvement in Segmentation Quality
2.Application to Various Domains
3.Integration with Other Techniques

## Slide 9
Analysis – 4W1H
Why: Bilevel 2D histogram-based image segmentation utilizes the joint distribution of pixel intensities to divide an image into distinct regions based on intensity relationships. This method is effective when intensity distributions are well-separated, allowing for clear and intuitive segmentation.
What: Bilevel 2D histogram-based image segmentation involves assessing threshold accuracy, performance metrics, and handling challenges like noise and complexity. Its effectiveness is evident in fields like medical imaging, remote sensing, and industrial inspection.
When: Analyzing bilevel 2D histogram-based image segmentation involves preparing images, analyzing the histogram, applying thresholds, and evaluating results. This ensures accurate and effective segmentation across diverse applications.
Where: Bilevel 2D histogram-based image segmentation is used in medical imaging, remote sensing, and industrial inspection to distinguish regions based on intensity distributions. It effectively separates distinct areas by analyzing pixel intensity relationships.
How: Bilevel 2D histogram-based image segmentation involves generating a 2D histogram to visualize pixel intensity distributions and applying two thresholds to classify pixels into distinct regions. This approach segments images by exploiting intensity relationships to differentiate between regions.
Refined Objective: Redefined objects analysis in bilevel 2D histogram-based image segmentation involves refining histogram analysis, applying advanced thresholding and segmentation methods, and enhancing results through post-processing. This approach ensures more accurate and meaningful object detection and delineation.

## Slide 10
Structural Diagram

## Slide 11
Use Cases & Testing
Use Cases
Medical Imaging: Segment tumors and organs in MRI/CT scans for diagnosis.
Remote Sensing: Classify land use and detect changes in satellite images.
Industrial Inspection: Identify defects and components in manufactured products.
Autonomous Vehicles: Detect objects and lanes for safe navigation.
Agriculture: Monitor crop health and detect weeds in aerial imagery.
Biometric Recognition: Detect faces and recognize fingerprints.
Image Retrieval: Improve search accuracy in image databases.
Test Cases
Simple Bimodal Image: An image with two distinct intensity levels (e.g., a synthetic image with two regions: one region with pixel values of 50 and another with pixel values of 200
Image with Gradual Intensity Variation: An image where intensity gradually changes from one side of the image to the other (e.g., a vignette effect).
Image with High Dynamic Range: An image with both very bright and very dark areas (high dynamic range).
Real-world Image with Shadows: A real-world image containing objects with shadows. The shadows introduce intermediate intensity values between the foreground object and background.
Textured Image Test Case: An image where texture causes local intensity variations within the same region (e.g., an image of grass or fabric).

## Slide 12
Implementation and Results – Iteration 1
Input Image: Grayscale image: Output image:
Ground truth Image

## Slide 13
Implementation and Results – Iteration 2
Input Image: Grayscale image: Output image:
Ground truth Image

## Slide 14
Team Progress and Movement
We have made significant progress on the Bilevel 2D histogram-based image
segmentation project, completing approximately 40-50% of the work. Key milestones
achieved include a comprehensive literature review, initial algorithm development, and preliminary testing on various image datasets. However, we are facing challenges as the segmentation results are not meeting expected accuracy levels, with issues such as varying intensity distributions and noise interference. To address these concerns, we will conduct in-depth data analysis, optimize the histogram thresholding parameters, and incorporate feedback from team members. Regular meetings will enhance collaboration and task delegation, ensuring we refine the segmentation algorithm effectively and continue to advance towards our project goals.

## Slide 15
Contribution
Individual Contribution
      Key contributions: Suchithra
      Algorithm Development and Implementation, and Data Analysis: Developed and implemented the Bilevel 2D Histogram-Based Image Segmentation algorithm, optimizing pixel brightness and local relative entropy. Collaborated with other team members to integrate the segmentation algorithm into existing image processing frameworks, focusing on improving segmentation accuracy.
      Key Contributions: Charisma
      Testing and Research: Gathered and prepared a diverse set of images to test the effectiveness of the segmentation algorithm. Conducted a detailed literature review on 2D histogram-based image segmentation techniques, examining their applications in various fields of image processing.
      Key Contributions: Sireesha
      Documentation: Documented the entire development process, including methodologies, challenges, and results, ensuring clear communication and traceability within the team. Created user guides and technical reports detailing the algorithm's usage and performance, aiding future research and development efforts.

## Slide 16
Conclusion & Future Work
Summary and Conclusion
The Bilevel 2D histogram-based image segmentation project is currently in its early implementation phase, with significant
progress made, but not all objectives have been fully realized. The team has encountered challenges such as varying intensity distributions, noise, and complex backgrounds, which have affected segmentation accuracy. To tackle these issues, the strategy
has been revised to focus on refining the histogram thresholding techniques and validating the method across different
image datasets. While the project is ongoing, these adjustments aim to enhance segmentation performance, leading to more
accurate and reliable image analysis outcomes.
Future Work
Future efforts will prioritize the optimization of histogram thresholding parameters to achieve better segmentation results.
Expanding the testing framework to include a wider variety of images from different domains will be essential for validating
the method's robustness. Additionally, integrating the segmentation tool into automated workflows and ensuring its usability
in practical applications will be crucial steps once the fundamental segmentation challenges are resolved.

## Slide 17
THANK YOU